Crack pass của Router CISCO

- Tắt bật lại router say khoảng 15 giây. Bấm tổ hợp phím Ctrl+Break. Route sẽ vào mode Rommom.

- Rommom1>confreg 0x2142 (thay đổi cấu trúc thanh ghi thành 2142)

- Rommom2>reset (khởi động lại router) Router sẽ bỏ qua giai đoạn kiểm tra pass.

- Khi router khởi động lại xong phải thay đổi lại pass mới.

- Thay đổi lại cấu trúc thanh ghi lại thành 2102 (Router(config)#config-register 0x2102)

- Lưu lại file cấu hình.

Crack pass Switch:

- Connect computer to the catalyst 2950 Switch using console cable.

- Plug console cable RJ-45 side into console port at back of the Switch, and DB-9 side into serial port at back of computer.

- Plug the power cable at back of the Switch, and Holding "mode" button at left corner of the front panel for 15 seconds

- In Windows XP,click "Start" menu,and then move to "Accessories"---->"Communications"---->"Hyper Terminal"

- The system has been interrupted prior to initializing the flash file system,and it wills show the following information.

- In command line, type "rename flash:config.text flash:config.old", it will rename the "config.text" configuration file in flash directory as "config.old". after rename, it will not boot from config.old

- In command line, type"boot". it will restart operating system and show the following information:

- In command line, type"boot". it will restart operating system and show the following information:

- Enter "n" at the prompt to start the Setup program.

- In command line, type "enable", it will enable privilege mode.

- type"rename flash:config.old flash:config.text" after "switch#_".

- type"copy flash:config.text run" in command line. it will copy the configuration to the current running-config file

- type"conf t" in command line , it will enable configuration terminal.

- type"no enable password" in command line , it will remove password

- type"no enable secret" in command line, it will remove secret

- type"line console 0" in command line. it changes to the console 0

- type"no password" in command line. it means do not set password for console 0

- type"end" in command line. it will save and quit config terminal mode

- type"write" in command line, it saves the configration file to running-config file. when next time start the switch, there is no password required